## Slide 1
Calibration aware neural pre-decoding
Real IBM calibration data, NVIDIA's pre-decoder and PyMatching, on one Alveo U55C
Nasir Ali, C-DAC Noida
Team walkthrough: run d = 1, 2, 3 and 5 yourself
Notes: Purpose: show the team how to run surface code memory experiments with real device calibration data, and what one FPGA card adds.

## Slide 2
2
Calibration aware pre-decoding on one U55C
From a calibration CSV to a decoded logical qubit
1
Calibration CSV
T1, T2, readout, sx and CZ or ECR error per qubit and coupler
calib/ibm_csv.py
2
Noise model
every fault location gets its own qubit's or coupler's rate
calib/noise.py
3
Syndromes
Stim samples detector events of a d x d x d window
Stim
4
Pre-decoder
NVIDIA Fast network, INT8, removes local errors
U55C card
5
Matching
PyMatching decodes what is left
harness/pipeline.py
No IBM account is needed: the eight device snapshots ship with qiskit-ibm-runtime (Apache 2.0) and are already exported to data/calibration/.
Notes: Each box is one module of the repository. The CSV is the only device specific input.

## Slide 3
3
Calibration aware pre-decoding on one U55C
What we found
44 of 54
d = 5 points where the INT8 pre-decoder significantly beats plain PyMatching
0 of 54
d = 5 points where it beats correlated PyMatching (51 significantly worse)
18 of 18
card runs bit exact against the integer model (both kernel instances)
2,330/s
d = 5 windows per second on one card (1.50 ms for a single window)
Strongest baseline wins at d = 5: PyMatching with correlations, no network at all, fails less often than pre-decoder + PyMatching on every device and setting.
Calibration matters: per qubit rates improve matching weights; and the network, trained on uniform noise, loses its gain when qubits differ strongly.
Honest limits: simulated circuits with calibrated rates, not runs on IBM hardware; the card is no faster than a large CPU for this small network.
Notes: Numbers come from results/summary.json; see the results section for the full picture. The key message: against correlated matching the pre-decoder does not pay at d = 5.

## Slide 4
4
Calibration aware pre-decoding on one U55C
Eight IBM devices, as calibrated
Medians over usable qubits and couplers, from data/calibration/*.csv
Device | Family | Snapshot | 2q gate | 2q error | Readout error | T1 (us) | T2 (us) | Readout (ns)
aachen | Heron r3 | 2026-04-17 | CZ | 0.15% | 0.74% | 232 | 255 | 2584
kingston | Heron r3 | 2026-04-15 | CZ | 0.18% | 0.95% | 283 | 144 | 2280
marrakesh | Heron r2 | 2025-02-26 | CZ | 0.32% | 0.95% | 197 | 118 | 2584
fez | Heron r2 | 2025-02-26 | CZ | 0.38% | 0.76% | 145 | 88 | 1560
torino | Heron r1 | 2025-02-26 | CZ | 0.41% | 2.29% | 185 | 141 | 1560
sherbrooke | Eagle r3 | 2025-02-26 | ECR | 0.75% | 1.97% | 279 | 169 | 1216
brisbane | Eagle r3 | 2025-02-26 | ECR | 0.77% | 2.00% | 232 | 150 | 1300
kyiv | Eagle r3 | 2025-02-26 | ECR | 1.15% | 1.27% | 287 | 118 | 1244
Readout errors are 3 to 10 times the two qubit errors, and data qubits idle through 1.3 to 2.6 us of readout: both dominate the noise.
Notes: Snapshot dates matter: Kingston and Aachen are April 2026, the others February 2025.

## Slide 5
Hands on
Set up once, then run d = 1, 2, 3 and 5 on a laptop

## Slide 6
6
Calibration aware pre-decoding on one U55C
Setup
git clone https://github.com/nasir26/u55c-calibrated-predecoder
cd u55c-calibrated-predecoder
python3.11 -m venv .venv && source .venv/bin/activate
pip install -r requirements.txt
# only for the full pre-decoder pipeline:
scripts/setup_reference.sh # NVIDIA code, pinned commit
HF_TOKEN=... scripts/fetch_weights.sh fast
pytest -q # tests
Laptop: steps 1 to 4 are enough for d = 1, 2, 3, 5.
Weights: accept NVIDIA's Open Model License on Hugging Face first.
Card: scripts/fetch_bitstreams.sh, then bench/run_card.py on a U55C host.
Notes: The teaching example needs only stim, pymatching and numpy. The full pipeline needs NVIDIA's code and the gated weights.

## Slide 7
7
Calibration aware pre-decoding on one U55C
Run d = 1, 2, 3, 5 in one command
python examples/small_codes.py \
data/calibration/ibm_kingston_2026-04-15.csv \
--d 1 2 3 5 --rounds 5 --scale 1
Chart: Logical error after 5 rounds, Kingston median noise
| d = 1 | d = 2 (kept shots) | d = 3 | d = 5
scale 1 | 5.371 | 0.18097 | 3.3295 | 1.526
scale 0.5 | 2.76 | 0.035819 | 0.952 | 0.2125
d = 1: one bare qubit; the bar every code must beat.
d = 2: detects but cannot correct: 51% of shots are thrown away at scale 1 to get the low rate shown.
d = 3, 5: decoded by PyMatching; larger d wins when the device is below threshold.
Notes: Same command for every distance. Scale 0.5 means a device with half of every error rate.

## Slide 8
8
Calibration aware pre-decoding on one U55C
What d = 1 and d = 2 can and cannot do
d = 1: no code
One physical qubit, measured at the end.
Every error in T1, T2 or readout is a logical error.
Error grows with the time it waits: the reference line.
d = 2: detection only
Four data qubits, three checks.
Any single error raises a flag, but two different errors raise the same flag.
So it can only discard flagged shots (post-selection); d = 3 is the smallest code that corrects.
Notes: Use this slide to explain detection versus correction.

## Slide 9
9
Calibration aware pre-decoding on one U55C
Run the full pipeline at d = 3 and 5
python bench/eval_ler.py \
--csv data/calibration/ibm_aachen_2026-04-17.csv \
--mode median --scale 1 --d 5 --basis X --shots 20000
Decoder | What it is
pm_cal | PyMatching with every qubit's own error rates
pm_median | PyMatching with the device medians only
fast_fp32 | NVIDIA Fast pre-decoder (float), then pm_cal
fast_int8 | integer pre-decoder, as on the card, then pm_cal
pm_corr | PyMatching with correlations (bench/eval_corr.py)
--mode: median, best (lowest error qubits) or screened (random, worst 10% removed).
--scale: 1 as calibrated; 0.5 halves every error rate.
Output: results/ler/<name>.json and per shot failure bits (.npz).
Notes: 200,000 shots at d = 5 take about 10 minutes on 8 CPU threads with the INT8 model; drop --shots for a quick look.

## Slide 10
10
Calibration aware pre-decoding on one U55C
Bring your own calibration CSV
Column | Used for
Qubit | row key
T1 (us), T2 (us) | idle noise over each layer
Readout assignment error | measurement flip
Prob meas1 prep0 | preparation flip (half)
Readout length (ns) | how long data qubits idle
√x (sx) error | one qubit gates
CZ error or ECR error | two qubit gates, "a_b:value;..."
Gate length (ns) | layer duration
Reset length (ns) (optional) | idle during reset
python calib/ibm_csv.py summary my.csv
python bench/eval_ler.py --csv my.csv ...
Headers are matched by keywords, so the IBM dashboard export loads as is.
Missing values mark a qubit unusable; it is never placed.
Notes: Any CSV in IBM's calibration layout loads; extra columns are ignored.

## Slide 11
Results
200,000 shots per basis and point; X and Z pooled

## Slide 12
12
Calibration aware pre-decoding on one U55C
At d = 5, correlated matching beats the pre-decoder
Failures of INT8 pre-decoder + PyMatching divided by each baseline; d = 5, median placement, as calibrated (scale 1)
Chart: 
| aachen | kingston | marrakesh | fez | torino | sherbrooke | brisbane | kyiv
vs PyMatching | 0.74049 | 0.91621 | 0.89528 | 0.87866 | 1.0493 | 1.0182 | 0.98975 | 0.96248
vs correlated PyMatching | 1.1856 | 1.2063 | 1.1407 | 1.1564 | 1.2958 | 1.2035 | 1.1624 | 1.1024
Teal below 1: the network removes errors plain matching gets wrong.
Amber above 1: correlated matching fixes the same errors, and more, without a network.
Putting the network in front of correlated matching does not help either.
Notes: Below 1 means pre-decoder plus PyMatching fails less often than the baseline. Teal: plain PyMatching. Amber: PyMatching with correlations, which needs no network.

## Slide 13
13
Calibration aware pre-decoding on one U55C
Where the pre-decoder still pays
Significant wins and losses of INT8 pre-decoder + PyMatching, all placements and scales
Baseline | d | points | pre-decoder better | pre-decoder worse | failure ratio range
PyMatching | 3 | 54 | 35 | 4 | 0.85 to 1.17
PyMatching | 5 | 54 | 44 | 4 | 0.64 to 1.06
correlated PyMatching | 3 | 54 | 21 | 12 | 0.73 to 1.20
correlated PyMatching | 5 | 54 | 0 | 51 | 1.07 to 1.61
d = 3, low noise: correlated matching gets worse than plain matching there; the network does not, so it wins.
Uneven qubits: on Kingston's screened placements it even makes plain matching worse (up to 17% more failures).
Notes: Counts are significant at p < 0.05 in a paired sign test over all placements and scales.

## Slide 14
14
Calibration aware pre-decoding on one U55C
Per qubit rates make PyMatching better
Failures with device median weights divided by failures with each qubit's own weights (best and screened placements)
1.04x
median ratio over all heterogeneous points
1.16x
largest ratio
39 of 60
points where median weights are significantly worse (p < 0.05)
The CSV is not only for simulation: its numbers become the matching weights.
This needs no network and no FPGA, only the calibration file.
Notes: With median placement both graphs are identical by construction, so only best and screened placements are shown.

## Slide 15
15
Calibration aware pre-decoding on one U55C
One U55C card
Same bitstream as the four card study; weights and window size are launch arguments
Chart: Windows per second (d rounds each)
| d = 3 | d = 5 | d = 7 | d = 9 | d = 11 | d = 13
windows per second | 4200.906 | 2329.808 | 1170.872 | 622.47 | 359.728 | 223.832
d | one window (ms)
3 | 1.05
5 | 1.50
7 | 2.34
9 | 3.84
11 | 6.21
13 | 9.56
Bit exact in 18 of 18 runs; logical failures from the card's bits equal the CPU integer model's shot for shot in 14 of 14 compared runs.
Notes: One card, both kernel instances, two launches in flight. Latency is one window through PCIe with XRT overheads, not a real time loop.

## Slide 16
16
Calibration aware pre-decoding on one U55C
What this is not
Not a hardware QEC run: no circuit ran on IBM devices; calibrations set the rates of a simulated circuit.
No chip embedding: IBM chips are heavy hexagonal; code qubits are placed by a rule, without SWAPs.
Model assumptions: depolarizing gates, T1 and T2 idle decay, half of Prob meas1 prep0 as preparation error; no leakage or crosstalk.
Not real time: card latency includes PCIe and runtime overheads; one big CPU is as fast for this network.
Notes: Say these out loud; they are also in docs/LIMITATIONS.md.

## Slide 17
Next steps
Try your own device CSV with examples/small_codes.py, then bench/eval_ler.py.
Fine tune the network on one device's calibrated noise, and compare with correlated matching.
Feed fresh calibrations daily and watch the decoder track drift.
Repository: github.com/nasir26/u55c-calibrated-predecoder
Notes: Ask the team which device CSVs they want to try next.